## Slide 1: Impacts of Model Grid resolutions
UNCLASSIFIED
UNCLASSIFIED
Environmental Systems
Modeling Team
Hailie Suk, PhD
Cold Regions Research and Engineering Laboratory (CRREL)
Engineer Research and Development Center (ERDC)
U.S. Army Corps of Engineers
CE-QUAL-W2 Water Quality Modeling Workshop
September 17-18, 2025

## Slide 2: CE-QUAL-W2 Model Grids
Waterbodies/Branches/Segments/Layers
Segments (a longitudinal segment of length ∆x)
Layers (a vertical layer of height ∆z).

## Slide 3: CE-QUAL-W2 Model Grids
Defining the spatial resolution (∆x and ∆z) for the model domain
∆x = 100 m to 1 km, ∆z = 0.5 – 1 m
Increasing spatial resolution can severe penalty in terms of turnaround time for running the model
Model results should not be a function of the grid resolution or the model timestep.
Model layer

## Slide 4: Model Grids - DeGray Reservoir
Branch length 30 km
Segment lengths 1000 m
Maximum width 5530 m
Layer height 2 m
Upstream segment 2
Downstream segment 31
∆z = 2m
∆z = 1m

## Slide 5: DeGray Bathymetry Files (2m, 1m, 4m)
segment lengths
water surface elevations
segment orientations
bottom friction
layer heights for each segment, and
average widths for each grid cell.
∆z = 2m
∆z = 1m
∆z = 4m

## Slide 6: DeGray Reservoir Elevation vs Volume
Chart: Elevation vs Volume
| 1506.585 | 1370.663 | 1238.463 | 1109.8409999999999 | 986.23299999999995 | 868.68 | 756.98199999999997 | 655.13199999999995 | 564.58199999999999 | 481.79599999999999 | 407.512 | 343.13600000000002 | 286.78199999999998 | 236.40600000000001 | 193.31 | 157.01599999999999 | 125.738 | 100.554 | 80.647999999999996 | 64.87 | 52.506 | 42.54 | 34.338000000000001 | 27.558 | 21.664000000000001 | 16.728000000000002 | 12.433999999999999 | 9.0459999999999994 | 6.5259999999999998 | 4.4379999999999997 | 2.7879999999999998 | 1.5940000000000001 | 0.80400000000000005 | 0.216
2m | 134.35 | 132.35 | 130.35 | 128.35 | 126.35 | 124.35 | 122.35 | 120.35 | 118.35 | 116.35 | 114.35 | 112.35 | 110.35 | 108.35 | 106.35 | 104.35 | 102.35 | 100.35 | 98.35 | 96.35 | 94.35 | 92.35 | 90.35 | 88.35 | 86.35 | 84.35 | 82.35 | 80.35 | 78.35 | 76.35 | 74.35 | 72.35 | 70.35 | 68.35
4m | 138.35 | 134.35 | 130.35 | 126.35 | 122.35 | 118.35 | 114.35 | 110.35 | 106.35 | 102.35 | 98.35 | 94.35 | 90.35 | 86.35 | 82.35 | 78.35 | 74.35 | 70.35
pre.opt created from the W2 preprocessor contains the model area-volume vs. elevation data.
Comparison of reservoir stage-volume curves for three model grids.

## Slide 7: DeGray Modeled Water Temperature Profiles
Chart: Temperature Profile at Jday = 200
| 33.758000000000003 | 33.372999999999998 | 32.936999999999998 | 27.852 | 20.286000000000001 | 15.598000000000001 | 12.436 | 10.964 | 10.157 | 9.7349999999999994 | 9.3610000000000007 | 8.9730000000000008 | 8.5990000000000002 | 8.2810000000000006 | 8.0440000000000005 | 7.8920000000000003 | 7.8079999999999998 | 7.77 | 7.7629999999999999 | 7.7629999999999999 | 7.7629999999999999 | 7.7629999999999999 | 7.7629999999999999
2m | 122.073 | 119.35 | 117.35 | 115.35 | 113.35 | 111.35 | 109.35 | 107.35 | 105.35 | 103.35 | 101.35 | 99.35 | 97.35 | 95.35 | 93.35 | 91.35 | 89.35 | 87.35 | 85.35 | 83.35 | 81.35 | 79.35 | 77.35
4m | 121.073 | 116.35 | 112.35 | 108.35 | 104.35 | 100.35 | 96.35 | 92.35 | 88.35 | 84.35 | 80.35 | 76.35
1m | 123.073 | 121.85 | 120.85 | 119.85 | 118.85 | 117.85 | 116.85 | 115.85 | 114.85 | 113.85 | 112.85 | 111.85 | 110.85 | 109.85 | 108.85 | 107.85 | 106.85 | 105.85 | 104.85 | 103.85 | 102.85 | 101.85 | 100.85 | 99.85 | 98.85 | 97.85 | 96.85 | 95.85 | 94.85 | 93.85 | 92.85 | 91.85 | 90.85 | 89.85 | 88.85 | 87.85 | 86.85 | 85.85 | 84.85 | 83.85 | 82.85 | 81.85 | 80.85 | 79.85 | 78.85 | 77.85 | 76.85 | 75.85
Chart: Temperature Profile at Jday = 100
| 13.935 | 13.83 | 13.644 | 13.006 | 12.951000000000001 | 12.86 | 11.57 | 9.9320000000000004 | 8.6969999999999992 | 8.4670000000000005 | 8.41 | 8.0579999999999998 | 7.8810000000000002 | 7.6989999999999998 | 7.55 | 7.4290000000000003 | 7.3449999999999998 | 7.2949999999999999 | 7.2720000000000002 | 7.2629999999999999 | 7.26 | 7.2560000000000002 | 7.2569999999999997
2m | 122.075 | 119.35 | 117.35 | 115.35 | 113.35 | 111.35 | 109.35 | 107.35 | 105.35 | 103.35 | 101.35 | 99.35 | 97.35 | 95.35 | 93.35 | 91.35 | 89.35 | 87.35 | 85.35 | 83.35 | 81.35 | 79.35 | 77.35
4m | 121.075 | 116.35 | 112.35 | 108.35 | 104.35 | 100.35 | 96.35 | 92.35 | 88.35 | 84.35 | 80.35 | 76.35
1m | 123.075 | 121.85 | 120.85 | 119.85 | 118.85 | 117.85 | 116.85 | 115.85 | 114.85 | 113.85 | 112.85 | 111.85 | 110.85 | 109.85 | 108.85 | 107.85 | 106.85 | 105.85 | 104.85 | 103.85 | 102.85 | 101.85 | 100.85 | 99.85 | 98.85 | 97.85 | 96.85 | 95.85 | 94.85 | 93.85 | 92.85 | 91.85 | 90.85 | 89.85 | 88.85 | 87.85 | 86.85 | 85.85 | 84.85 | 83.85 | 82.85 | 81.85 | 80.85 | 79.85 | 78.85 | 77.85 | 76.85 | 75.85

## Slide 8: DeGray Modeled Dissolved Oxygen (DO) Profiles

## Slide 9: Detroit Lake W2 Model
The W2 model segments were modified to reduce the total number of segments (66  36).
When significantly coarsening a model grid, some of the finer details of the flow and temperature dynamics were lost.
The final model chosen (shown in yellow) tracked the original outlet temperatures (shown in black) very well.
Courtesy of Scott Wells

## Slide 10: Hands-on Exercises
Review the differences of bathymetry files from “DeGray W2 Project”
  Layer height = 2 m (bth1.csv)
  Layer height = 1 m (bth1-1m.csv)
  Layer height = 4 m (bth1-4m.csv)
Compare the differences of following predicted results for the 2 m, 1 m and 4 m layer heights
  water temperature and dissolved oxygen profiles (spr.csv)
  withdrawal output (two_31.csv)

## Slide 11: Questions?