## Slide 1: MODEL SETUP I: LECTURE
UNCLASSIFIED
UNCLASSIFIED
Environmental Systems Modeling Team
Hailie Suk, PhD
Cold Regions Research and Engineering Laboratory (CRREL)
Engineer Research and Development Center (ERDC)
U.S. Army Corps of Engineers
CE-QUAL-W2 Water Quality Modeling Workshop
September 17-18, 2025

## Slide 2: Outline
Background
Definition of problem
Required Information
  Bathymetry
  Flow
  Meteorology
  Observations
  Other
Output
Detroit Dam, Oregon

## Slide 3: Background
Setting up a computational model is an effort to create a computational approximation of a real system.
A model enables one to investigate past behavior or future conditions with regard to changes in conditions.
Approximations, simplifications, and omissions are necessary but must be balanced with regards to the model’s ability to accurately capture the behavior of the real system.

## Slide 4: How to Set Up and Run a Model Application

## Slide 5: Definition of Problem
What are water quality issues occurring in system that warrant a model?
Are they the result of:
  Flow alterations?
  Operations?
  Boundary Loadings?
  Intermediate loadings?
  Meteorology?
  Altered system conditions?
  Anticipated future changes in any of above?
  Other?
What information is required to set up a model to capture the behavior in question?
Source: https://www.erdc.usace.army.mil/Media/Images/igphoto/2002471 393/

## Slide 6: Bathymetry
Defines the physical structure of the natural system for the model
Sources
  Sediment range surveys
  Cross Sections
  Pre-impoundment surveys for reservoirs
Extent
  All of area of concern and beyond
  Reaching upstream to control point
Resolution
  Horizontal (across system) – meters
  Longitudinal (along system) – 10s or meters or more
  Vertical (through water column) – meter or less

## Slide 7: Flow
Required
  Headwater
  Downstream
  Tributary
  Withdrawals
Water surface elevations

## Slide 8: Meteorology
Reliable data is essential to model performance, accuracy of model results, and validity of any concepts developed from model.
There is no substitute for good met data.
Typical sources are airports in vicinity of project.
If available multiple airports may be used to evaluate model sensitivity.
Class A
Required information:
  Air Temperature
  Dew Point Temperature
  Wind Speed
  Wind Direction
  Cloud Cover
  Solar Radiation

## Slide 9: Observations
Observed data
  For all water quality constituents
  Provides Boundary conditions
  Calibration
Analysis provides insight as to what is occurring in system PRIOR to modeling.
Aids in refinement of modeling approach.

## Slide 10: Other
Loadings
  Point source
  Non-point source/runoff
  Other forms of water quality constituent loads
Sediment
Operations records
  Which gates used for how long
  Power generation
  Spills
  Anything else that impacts water movement

## Slide 11: Output
Identify what information is desired from model output.
Ensure that it is being output at times and locations desired.
Process and evaluate model output and compare to applicable observations.

## Slide 12: Questions?